This describes 1) contents of the attached matlab and excel files and shapefiles, 2) estimates of freshwater input to Hood Canal, 3) dissolved, particulate and total N and C concentrations and loads, 4) total dissolved N (TDN) concentrations and loads with population removed or doubled.

Shapefiles:

- HCDOP_sampled_tributaries.shp: A shape file of 39 points for the HCDOP- sampled tributary locations.  ~44 sites have been sampled, but this file contains only the sample points needed for loading calculations (i.e. sample sites upstream of other sample sites are not included).  In some cases, the point is inland, off the shoreline, and may need to be moved towards the shoreline for the marine model.  The site KOKA (Lake Kokanee) is the point at Lower Cushman Dam, near the intake for the Cushman generation flows.  The points in this file are the same 39 sample locations in the excel worksheet and Matlab workspace.

- Unsampled_Polygons_FINAL2.shp: A shape file of 10 polygons that include all Hood Canal watershed area not sampled by HCDOP.  This includes undifferentiated shoreline catchments and a few small streams on Kitsap Peninsula and other low elevations (e.g. Rendsland Creek).

Excel file:

- hc_freshwater_2005_06_loads_conc2.xls:  This excel file contains separate worksheets for the 2005 – 2006 observed DOC, POC, TOC, NO3, NO2, NH4, TDN, PN, and TN concentrations and loads from the 39 rivers and 10 unsampled polygons in the 2 shapefiles above.  Units for the concentrations worksheets are all ug/L C or ug/L N.  Units for the loads worksheets are metric tonnes per month.  The sheets “TDN_load_no_people”, “TDN_conc_no_people”, “TDN_load_2times_people”, and “TDN_load_2times_people” have the results of the human impact scenarios (described below).

The sheet “Flows_m3s” has river flows from 39 rivers and estimated surface and subsurface flow from the 10 shoreline polygons, all in m3/s.  These flows/loads are intended to include all surface and subsurface freshwater input from these areas.  Summing the 10 shoreline polygons flows/loads and those of the 39 river sampling points will account for all freshwater input other than rain directly on the Hood Canal surface.

Matlab file:

- hc_freshwater_2005_06_loads_conc2.mat:  This Matlab workspace has the same information as the excel file, except for the summary table (Table 3 below).

2005 – 2006 N and C Loads/Concentrations in Excel file and Matlab Workspace

Flows: Flows from the 39 catchments and 10 shoreline polygons are shown in the excel worksheet (“Flows_m3s”).  These flows include all gage data from all sources.  When gage data where unavailable, flow was estimated using a specific yield method.   For each day in the hydrologic record, gaged daily mean flows were drainage area normalized, and the arithmetic mean of the daily specific yields in Kitsap/Lowland region was applied to ungaged Kitsap/Lowland watersheds:

,

with i=1 to n streams in the region with flow data available for a particular day.  The two figures below show the different hydrologic regions and the sampled and unsampled area.

Figure 1.  Watersheds sampled by HCDOP are shown in color.  The hatched region is the unsampled area.  The four populated watersheds shown in black (Big Beef, Seabeck, Union, Tahuya) were used to estimate N and C concentrations in the unsampled area.

Concentrations: Dissolved, particulate, and total N and C 2005 – 06 monthly concentrations and loads measured at 39 tributary sites are in the attached excel worksheet, matlab workspace, and summarized in tables below.  The unsampled area in aggregate has a population density similar to that of Big Beef (83.1 people/km2), Seabeck (61.4 people/km2), Tahuya (19.5 people/km2), and Union River (33.3 people/km2) watersheds.   The monthly arithmetic mean of concentrations measured in these 4 populated Kitsap watersheds was used as a monthly estimated concentration for the unsampled catchments.  The mean of these 4 watersheds’ population densities is 49 people/km2.  The unsampled catchments in the Hood Canal watershed have a population density of 45.3 people/km2.  For simplicity, this concentration is used for the entire unsampled area (all 10 sub-regional polygons in the shapefile).  Thus, N and C loads from each of the 10 shoreline polygons differ only because of their flows.

| Table 1. Regional flow-weighted mean concentrations, annual loading rates, and area - normalized loading rates based on 2005 - 06 HCDOP monthly grab samples. |
| --- |
| Flow-Weighted Mean Concentrations (ug/L) |  |  |  |  |  |  |  |  |
|  | NO3 | NH4 | NO2 | DIN | DON | TDN | PN | TON | TN |
| N Fork Skokomish Diversion | 22 | 10.0 | 0.4 | 33 | 38 | 72 | 36 | 75 | 108 |
| Skokomish River | 71 | 9.5 | 2.9 | 83 | 22 | 106 | 81 | 103 | 186 |
| Sampled Kitsap/Lowland Watersheds | 198 | 12.7 | 0.9 | 212 | 72 | 283 | 37 | 108 | 319 |
| Unsampled Kitsap/Lowland Watersheds | 325 | 12.7 | 1.0 | 339 | 114 | 452 | 43 | 157 | 495 |
| Other Olympic Mountain Rivers | 61 | 7.6 | 0.4 | 69 | 38 | 108 | 34 | 72 | 142 |
| Flow - Weighted Mean Concentration (ug/L N): All Hood Canal tributaries | 97 | 9.5 | 1.2 | 108 | 44 | 152 | 49 | 93 | 201 |
| Loads (Metric Tonnes/Year) |  |  |  |  |  |  |  |  |  |
|  | NO3 | NH4 | NO2 | DIN | DON | TDN | PN | TON | TN |
| N Fork Skokomish Diversion | 14 | 6.2 | 0.23 | 20 | 24 | 44 | 22 | 46 | 67 |
| Skokomish River | 95 | 12.8 | 3.95 | 111 | 30 | 141 | 109 | 139 | 250 |
| Sampled Kitsap/Lowland Watersheds | 86 | 5.5 | 0.37 | 92 | 31 | 122 | 16 | 47 | 138 |
| Unsampled Kitsap/Lowland Watersheds | 144 | 5.6 | 0.42 | 150 | 50 | 199 | 19 | 69 | 218 |
| Other Olympic Mountain Rivers | 109 | 13.5 | 0.63 | 124 | 68 | 192 | 60 | 128 | 252 |
| Total Annual Load | 447 | 44 | 5.6 | 496 | 202 | 699 | 226 | 429 | 925 |

| Table 2. Regional flow-weighted mean concentrations, annual loading rates, and area - normalized loading rates based on 2005 - 06 HCDOP monthly grab samples. |
| --- |
| Flow-Weighted Mean Concentrations (ug/L) |  |  |  |  |
|  | DOC | POC | TOC |  |  |
| N Fork Skokomish Diversion | 836 | 396 | 1232 |  |  |
| Skokomish River | 473 | 871 | 1344 |  |  |
| Sampled Kitsap/Lowland Watersheds | 2180 | 355 | 2535 |  |  |
| Unsampled Kitsap/Lowland Watersheds | 2352 | 388 | 2740 |  |  |
| Other Olympic Mountain Rivers | 869 | 310 | 1180 |  |  |
| Flow – Weighted Mean Concentration: All Hood Canal tributaries | 1016 | 496 | 1512 |  |  |
| Loads (Metric Tonnes/Year) |  |  |  |  |  |
|  | DOC | POC | TOC |  |  |
| N Fork Skokomish Diversion | 514 | 244 | 758 |  |  |
| Skokomish River | 635 | 1176 | 1811 |  |  |
| Sampled Kitsap/Lowland Watersheds | 945 | 153 | 1098 |  |  |
| Unsampled Kitsap/Lowland Watersheds | 1038 | 171 | 1209 |  |  |
| Other Olympic Mountain Rivers | 1549 | 555 | 2104 |  |  |
| Total Annual Load | 4681 | 2299 | 6980 |  |  |

Population Effects on N export: Multiple regression models showed the variation among watersheds’ 2-year flow-weighted mean DIN concentrations could be explained by 1) land cover and population density, 2) land cover alone, or 3) soil and physical characteristics alone (publication in progress).  Similar sets of significant factors were found in multiple regression models for TN and TDN.  Overall, the models showed that land cover and population density effects on concentration are similar in magnitude.  The multiple regression models are of limited utility in population scenario analyses since they explained less than 55% of the variance in concentrations.  When all terms were included in the model, a large bias (over-prediction) in loads resulted, even though the models had zero mean bias in predicting concentration.   [More detail on statistics results can be provided later in the summer].

A simple N mass balance approach was selected for developing scenarios for human effects on N loads.  Seven septic N loading papers reviewed by Horowitz et al. (the septic bootstrap model started in Mike Brett’s class) reported average TN outputs of approximately 4 kg/person/year.  To simulate a much reduced human disturbance scenario, similar to the effect of removing nearly all human N input, each watershed’s TDN loads were reduced by 4 kg/year for each person.

Each stream and shoreline’s estimated annual load reduction was subtracted from the observed 2005 – 2006 annual TDN load.  The result was a lower annual TDN load that was distributed among calendar months based on the observed 2005 – 06 monthly TDN load seasonality.  For example, on average, 20.8% of TDN export in 2005 and 2006 occurred in January, so 20.8% of the reduced annual load was assumed to be exported in January.  Concentrations of TDN under the reduced human impact scenario were calculated inversely, based on the estimated reduced TDN loads.  In four small streams, subtracting the annual load reduction from the observed TDN load resulted in a negative annual load and negative monthly loads and concentrations.  For example, Big Beef Creek had an average 2005 – 2006 TDN load of 12.8 metric tonnes, and 4 kg TDN/year per person in the watershed summed to 14.6 metric tonnes.  The 4 streams’ negative annual loads summed to 2.2 metric tonnes (<0.5% of the total reduced TDN loads), and are unlikely to affect overall conclusions.

Effects of population doubling were estimated by a similar method, with each new person adding 4 kg TDN/year to watersheds’ 2005 – 2006 loads.  This simulated a TDN effect of same magnitude (205.5 metric tonnes) as the reduced disturbance scenario (Table 3).  The population/TDN effect scenarios are intended to be “best” and “worst” case possible scenarios (e.g. no denitrification of septic N).

Table 3.  Estimated annual TDN and TN loads as observed in 2005 – 2006 and with a removal of 4 kg TDN/person/year.  All units are metric tonnes/year.

|  | 2005 - 2006 TDN loads | 2005 - 2006 TDN loads Removing all population (4 kg/person/year) | 2005 - 2006 TDN loads Doubling population (4 kg/person/year) | 2005 - 2006 PN loads |
| --- | --- | --- | --- | --- |
| 39 HCDOP sampled rivers | 499.8 | 425.8 | 573.8 | 207.5 |
| Shorelines and other unsampled areas | 199.2 | 67.8 | 330.6 | 19.0 |
| Total | 699.0 | 493.5 | 904.4 | 226.5 |
| Total N load observed | 925.4 |  |  |  |
| Total N load without people | 720.0 |  |  |  |
| Total N load with population doubling | 1130.9 |  |  |  |